## Slide 1: Compliance Inspections of Natural Gas Systems

## Slide 2: Safety Regulations Applicable to Natural Gas Systems
Who are these people and why are they calling me?
Where do they get their authority?
Notes: A new operator might have these questions.
Federal Inspectors are responsible for inspecting Interstate, and some Intrastate, pipeline facilities in the United States.
State Inspectors are agents of the Federal Government who inspect Intrastate, and in some cases Interstate, pipeline facilities.

## Slide 3: USC Section 60117
(c) – Entry and Inspection
  By displaying proper credentials, inspectors have the right to enter the premises
  Inspect records and property
  Reasonable time and manner

## Slide 4: Safety Regulations Applicable to Natural Gas Systems
49 CFR 192 - The Minimum Federal Safety Standards Applicable to the Transportation of Natural Gas and for Pipeline Facilities Used for this Transportation
Notes: Note that these are the MINIMUM federal safety standards applicable to natural gas systems. An operator must meet the minimum requirements of the code listed under Part 192 to comply with the pipeline safety regulations.

## Slide 5: Safety Regulations Applicable to Natural Gas Systems
Authority: Natural Gas Pipeline Act of 1968 (49 U.S.C. sec. 1671 et seq.)
Re-Authorized by the Securing America's Future Energy: Protecting our Infrastructure of Pipelines and Enhancing Safety Act (SAFE PIPES Act) on March 3, 2016
Notes: The pipeline safety regulations were created to provide minimum operation and maintenance safety standards for operators of natural gas systems.
These minimum standards were put in place to protect the public, customers, and natural gas system employee’s.
Always remember our goal is to PROTECT PEOPLE FIRST!

## Slide 6: Part 190 Regulatory Authority
§190.203 Inspections and Investigations.
  Upon presenting appropriate credentials authorized to enter upon, inspect, and examine, at reasonable times and in a reasonable manner, the records and properties of persons to the extent such records and properties are relevant to determining the compliance of such persons with the requirements of 49 U.S.C. 60101 et seq., or regulations, or orders issued there under.
Notes: An operator may ask who has the authority to do an inspection of my system, and where did they get it? The authority was given to PHMSA by congress under the pipeline safety laws for transportation of hazardous materials by pipeline.

## Slide 7: Part 190 Regulatory Authority
§190.203 Inspections and Investigations.
  Inspections are ordinarily conducted
    (1) Routine scheduling
    (2) A complaint from a member of the public
    (3) Information obtained from previous inspection
    (4) Report from a State agency participating in the Federal Program under 49 U.S.C. 60105
    (5) Pipeline accident or incident
    (6) Whenever deemed appropriate
Notes: Inspections may be conducted at different times and for different reasons by PHMSA or a state agency acting as an agent for PHMSA. State programs under such an agreement are audited by PHMSA on an annual basis to verify their program performance.

## Slide 8: How Do I Prepare for an Inspection?
What do I do?
Where do I begin?
What do I look for?
What’s the inspector going to look at and for?
Notes: These are some of the questions an operator may ask himself prior to an inspection by either PHMSA or the state agency that has jurisdiction over their facilities.

## Slide 9: What Type of Inspector Will I Get?
What an inspector will focus on may vary depending on their personality, work background, or recent industry events.
Inspector looking at facts to determine compliance
Notes: What type of inspector will I get? This can be a very subjective question, inspectors are people with a job to do just like you. Most inspectors are just there to do their jobs the same as you are. An operator who works with the inspector, provides the needed documentation, and answers questions honestly and to the best of his ability, will likely have a cordial audit. This is not to say you won’t have a violation, but remember you are all professionals. It doesn’t help anyone to get angry or upset with the inspector if he finds a problem on your system, that is his job to make sure you the operator are in compliance.

## Slide 10: What Type of Inspection Will I Get?
Clarify the type, dates and
location of the inspection!
Notes: What type of inspector will I get? This can be a very subjective question, inspectors are people with a job to do just like you. Most inspectors are just there to do their jobs the same as you are. An operator who works with the inspector, provides the needed documentation, and answers questions honestly and to the best of his ability, will likely have a cordial audit. This is not to say you won’t have a violation, but remember you are all professionals. It doesn’t help anyone to get angry or upset with the inspector if he finds a problem on your system, that is his job to make sure you the operator are in compliance.

## Slide 11: Where Do I Begin?
Think like an inspector
  Code requirements and not just company requirements
  Current operator name, operator identification number, operator official, address, and contact information
Notes: To do an inspection you must think like an inspector. If you go in with the mindset that everything is right because we’ve always done it this way and never had a problem, then you may be in for a few surprises when you have your audit.

## Slide 12: Where Do I Begin?
Think like an inspector
  Current forms
  Forms available at:
  http://phmsa.dot.gov/pipeline/library/forms
  Standard, OQ, IM, Public Awareness, accident, control room management inspection forms are all available on the website
Notes: To do an inspection you must think like an inspector. If you go in with the mindset that everything is right because we’ve always done it this way and never had a problem, then you may be in for a few surprises when you have your audit.

## Slide 13: Where Do I Begin?
A complete, up-to-date operations and maintenance manual
  Right company information
  Most recent version
  Procedures and processes for safely performing operations and maintenance tasks your system
  Employee access
Notes: To do an inspection you must think like an inspector. If you go in with the mindset that everything is right because we’ve always done it this way and never had a problem, then you may be in for a few surprises when you have your audit.

## Slide 14: Where Do I Begin?
A complete, up-to-date operations and maintenance manual
  Manual have procedures for handling emergencies
    Emergency response procedures.
    Actions directed toward people first
Notes: To do an inspection you must think like an inspector. If you go in with the mindset that everything is right because we’ve always done it this way and never had a problem, then you may be in for a few surprises when you have your audit.

## Slide 15: Where Do I Begin?
  Complete and up-to-date damage prevention plan
  Complete and up-to-date public awareness plan
  Up-to-date operator qualification plan
    Employee qualifications
  Up-to-date drug and alcohol plan
  Control room management
  Integrity management plans
  Training records
Notes: To do an inspection you must think like an inspector. Make sure that all of your documentation is up to date or current. Most operations and maintenance tasks which are required by the code, have a required time frame for compliance. The inspector will want to see the documentation to show when these tasks were performed, who performed them, and the record of the previous inspection, to determine the required time frames were met.

## Slide 16: Where Do I Begin?
Recent incidents or safety related conditions
One call notices
Annual report
Notes: To do an inspection you must think like an inspector. The key to having a good inspection is to maintain proper records and documentation of operations and maintenance tasks which are required by the code. The key point to remember is “If you didn’t document it, then you didn’t do it”.

## Slide 17: Where Do I Begin?
All of the records required by the code for your system.
Company records contain all code required information for your system
Notes: To do an inspection you must think like an inspector. The key to having a good inspection is to maintain proper records and documentation of operations and maintenance tasks which are required by the code. The key point to remember is “If you didn’t document it, then you didn’t do it”.

## Slide 18: Where Do I Begin?
Clarify what records to be reviewed and time period
Know where the records are located
If you didn’t document it, then you didn’t do it!

## Slide 19: Where Do I Begin?
Make sure records are complete and up-to-date.
  What work was performed? (New Const., Repair, O&M Task)
  Who performed the work? (Company or Contractor) (OQ)
  When was the work performed? (Date & Time)
  Where was the work performed? (System, Line Segment, Station)
Notes: To do an inspection you must think like an inspector. The key to having a good inspection is to maintain proper records and documentation of operations and maintenance tasks which are required by the code. The key point to remember is “If you didn’t document it, then you didn’t do it”.

## Slide 20: Where Do I Begin?
Make sure records are complete and up-to-date.
  Maps, red lines of recent work
  Check dates, versions
  Revision history if looking at procedures
Notes: To do an inspection you must think like an inspector. The key to having a good inspection is to maintain proper records and documentation of operations and maintenance tasks which are required by the code. The key point to remember is “If you didn’t document it, then you didn’t do it”.

## Slide 21: Where Do I Begin?
Use the tools and inspector will use.
  Use a current and up-to-date code book.
  Download the most current code book from the PHMSA website
Use a federal inspection report sheet.
Notes: To do a proper inspection you must have the proper tools. You must have an up-to-date copy of the 192 code book, and the latest revision of the PHMSA Inspection Form.

## Slide 22: Where Do I Begin?
For standard inspection
  Corrosion records
  Compressor stations
  Regulator stations
  Damage prevention and one call
  Patrolling and leakage surveys
  Valve inspections

## Slide 23: Things to Remember when being inspected
Have your records available
Know who to call if additional information is needed
Recognize that the inspector is there to do a job

## Slide 24: Things to Remember when being inspected
The inspection is a legal proceeding
  Answer the questions to the best of your ability
  If you do not know the answer to a question – tell them that you don’t know
Be prepared to disagree
Inspector has a right to documents to prove non-compliance

## Slide 25: What Happens When the Inspection is Over?
The inspector will generally have a meeting with the operator to close out the inspection.
The inspector will go over their findings with the operator, and describe what is out of compliance with the code (if anything) and why.

## Slide 26: What Happens When the Inspection is Over?
What the inspector lists as issues found in the audit may or may not be found in the final letter from the state program manager or PHMSA regional director.
The inspector is a fact finder and will make recommendations to their directors.
The enforcement authority lies with the state program manager or PHMSA regional director, and that’s who will send the letter.

## Slide 27: Other Forms
  Operator Annual Report Forms
  Operator Incident Report Forms
  Incident Investigation Inspection Forms
  Operator Qualification Inspection Forms
  Drug and Alcohol Program Inspection Forms
  Integrity Management Inspection Forms
  Construction Inspection Forms
Notes: Inspections may be conducted at different times and for different reasons by PHMSA or a state agency acting as an agent for PHMSA. State programs under such an agreement are audited by PHMSA on an annual basis to verify their program performance.

## Slide 28: Information Websites
PHMSA Training and Qualification
http://www.phmsa.dot.gov/pipeline/tq
PHMSA Pipeline Safety Regulations
http://www.phmsa.dot.gov/pipeline/tq/regs
PHMSA Pipeline Safety Forms
http://www.phmsa.dot.gov/pipeline/library/forms
Notes: You can also access Small Operator Manuals and Guides, Advisory Bulletins, Alert Notices, Rule Interpretations, and much more from the PHMSA Website.

## Slide 29: Thanks!
??????
Bryan Kichler
PHMSA T&Q
Bryan.kichler@dot.gov